## Slide 1: Module 3
Instruction Set Architectures

## Slide 2
Instruction Set Architecture
Encompasses all the information necessary to write a machine language program that will run correctly, including instructions, registers, memory access,
I/O, and so on.
The words of a computer's language are called instructions, and its vocabulary is called an instruction set.

## Slide 3
Different Types of Architecture Classification
RISC and CISC
Accumulator based ,Stack based, General purpose registers

## Slide 4: INSTRUCTION TYPES- Format of Instructions
INSTRUCTION TYPES refer to the format of instructions
Classified based on the number of operands used in the instruction
The classification includes:
  Three address instructions
  Two address instructions
  One address instructions
  Zero address instructions
USES THREE TYPES OF ARCH.
1.STACK
2.ACCUMULATOR
3.GENERAL PURPOSE REGISTERS

## Slide 5: Three Address Instructions
C=A+B
C [A]+[B]
We will use the variable names to the corresponding memory location
ADD A, B, C
OPERATION SOP1 SOP2 DEST OP
A AND B ARE SOURCE ,C IS DESTINATION
CONTENTS OF A AND B ARE ADDED UP AND STORED IN C
If 32 bit of computer is used then to perform addition operation we require 3k bits and it is too large to fit in one word

## Slide 6: TWO ADDRESS INSTRUCTION
ADD A,B
A IS SOURCE ,B IS ACTING AS SOURCE AND DEST.
MOVE B,C
ADD A,C
NOW THE VALUE OF B IS UNCHANGED
If 32 bit of computer is used then to perform addition operation we require 2k bits and it is too large to fit in one word

## Slide 7: ONE ADDRESS INSTRUCTION
IMPLICIT LOCATION VIA ACCUMULATOR
Load A -------------- moves the contents of A to Accumulator (Implied)
Add B -------------- A and B gets added up
Store C -------------- From Accumulator to memory
USE of General Purpose Registers
Add Ri , Rj
Add Ri , Rj , Rk
Move A, Ri same as Load A, Ri
Move Ri, A same as Store Ri, A
Number of bits needed to specify a register is much less than that of a memory location, Eg., 5 bits are required for 32 registers
Register usage allows faster processing

## Slide 8: INSTRUCTION TYPES
C=A+B
Using Operands from processor registers:
Move A,Ri
Move B,Rj
Add Ri,Rj
Move Rj,C
………………………………………..
Using One Operand from memory:
Move A,Ri
Add B,Ri
Move Ri,C

## Slide 9: INSTRUCTION TYPES
ZERO ADDRESS INSTRUCTION
PUSH A
PUSH B
ADD
POP C

## Slide 10: Accumulator architecture
Accumulator
ALU
Memory
registers
address
latch
latch
Example code: a = b+c;
load b; // accumulator is implicit operand
add c;
store a;

## Slide 11: Stack architecture
Example code: a = b+c;
push b;
push c;
add;
pop a;
b
b
c
b+c
push b
push c
add
pop a
stack:
ALU
Memory
stack
stack pt
latch
latch
latch

## Slide 12: Other architecture styles
Stack Architecture | Accumulator Architecture | Register-Memory | Memory-Memory | Register (load-store)
Push A | Load A | Load r1,A | Add C,B,A | Load r1,A
Push B | Add B | Add r1,B |  | Load r2,B
Add | Store C | Store C,r1 |  | Add r3,r1,r2
Pop C |  |  |  | Store C,r3
Let's look at the code for C = A + B

## Slide 13: INSTRUCTION TYPES
Program to evaluate X = (A + B) * (C + D)

## Slide 14: Three Address Instructions
Computers with three address instruction formats can use each address field to
specify either processor registers or memory operands
Program to evaluate X = (A + B) * (C + D)
ADD R1, A, B R1  M[A] + M[B]
ADD R2, C, D R2  M[C] + M[D]
MUL X, R1, R2 M[X]  R1 * R2
Results in short programs
Instruction becomes long (many bits)

## Slide 15: Two Address Instructions
Program to evaluate X = (A + B) * (C + D)
MOV R1, A R1 M[A]
ADD R1, B R1  R1 + M[A]
MOV R2, C R2  M[C]
ADD R2, D R2  R2 + M[D]
MUL R1, R2 R1  R1 * R2
MOV X, R1 M[X]  R1

## Slide 16: One Address Instructions
Use an implied AC register for all data manipulation
Program to evaluate X = (A + B) * (C + D)
LOAD A AC  M[A]
ADD B AC  AC + M[B]
STORE T M[T]  AC
LOAD C AC  M[C]
ADD D AC  AC + M[D]
MUL T AC  AC * M[T]
STORE X M[X]  AC

## Slide 17: Zero Address Instructions
Can be found in a stack-organized computer
No need of address field for ADD and MUL instruction
PUSH and POP requires address field to specify the operand that communicate with the stack
Program to evaluate X = (A + B) * (C + D)
PUSH A TOS  A
PUSH B TOS  B
ADD TOS  (A + B)
PUSH C TOS  C
PUSH D TOS  D
ADD TOS  (C + D)
MUL TOS  (C + D) * (A + B)
POP X M[X]  TOS
Note: To evaluate arithmetic expression in a stack computer, it is necessary to
convert the expression into reverse polish notation .